## Slide 1: Winter Flying
VFR/IFR
Tom Halvorson CFII

## Slide 2: Winter Flying
The Beauty
Blue Sky guidance
Cleaning the pad/plane
Flight considerations
Destination planning specific to Winter related issues

## Slide 3: Winter Flying
The winter months can bring beautifully smooth, dense air that truly makes flying enjoyable.
Great engine performance
Great climb rates
But…

## Slide 4: BSAA Guidance
Pre-heating required if the temperature has been below 32 degrees within the previous two hours of flight and plane was not recently flown
  Do you know how to use the preheater - Turn fan on first and turn off last after shutting off fuel
  Don’t leave preheater unattended and keep temperature around 250 degrees
  If cylinders feel warm, that is sufficient preheating
  Plug in battery in the shed after use and notify Bill Sundburg if low on propane

## Slide 5: BSAA Guidance
Keep fuel tanks full to minimize water condensation in the tanks
Do not run battery down
Crank starter for 10 seconds with 30 a second wait between cranks
Aircraft are 24 volts, do not try to jump start from a car and secure appropriate maintenance to jump start the engine
  Read the POH before jump starting
If unable to start the plane, advise Bill Sundburg or other board member

## Slide 6: BSAA Guidance
Deice wing surface if frost is on the wings
  NEVER SCRAPE WINGS OR GLASS WITH A SCRAPER
  Use windshield washing solution in the shed
Propellers should point down after tie down
  This is to ensure any melted ice/snow does not refreeze in the prop spinner
  Always be cautious when moving the prop – move it back words
Be cautious about ice on taxiways and high snowbanks – example Greenwood Lake
If taxing on the grass, ensure it is solid enough to taxi on
If using the tug, ensure it is plugged into to the charger after use

## Slide 7: Shoveling
If it has snowed recently bring a shovel
Use the snow blower in the shed
  Be careful which way you blow the snow – not at the plane
  Clean off the entire pad and don’t leave a pile of snow in front of the planes by the taxi way as prop may hit the ice
Don’t use a scraper on the glass or airframe

## Slide 8: Winter Flight considerations
Dress appropriately
  Consider time outside while preheating or clearing the plane
  Consider your protection in the unlikely event of an airport landing
Make sure oil temperatures are in the green before flight and before high RPM’s
Be aware of carbon monoxide poisoning – monitor the CO detector

## Slide 9: Winter Flight considerations
What are signs of airframe icing?
Where is the worst airframe icing risk?
  Below the clouds?
  In the middle of the clouds?
  At the top of the clouds?
When does most icing occur?
  On approach, climb or cruise?

## Slide 10: Winter Flight considerations
Exercise caution due to inflight icing
  Have you done an appropriate briefing, particularly for clouds, temperatures aloft, Airmet Zulu and pilot reports
    Ice can also occur below clouds – freezing rain
  What is your “OUT” in the even you experience airframe icing
  Consider Pitot heat if temps are below 5 degrees C
  Static system ice can occur – Activate alternate static air
  Alternate induction air – Only Diamond – Skyhawk is automatic
    Static air effects static instruments; alternate induction air is engine performance

## Slide 11: Winter Flight considerations
Signs of airframe icing
  Visible on leading edges and particularly small surfaces, e.g., horizontal stabilizer
  Loss of power due to carburetor ice or induction ice
  Loss of lift – may not be able to maintain level flight
  Communications could become difficult due to ice on antennas
Descend to lower temperatures – get out of the clouds
  Climbing above clouds can be dangerous
  If airframe is iced over do not use flaps and keep speed a little faster on approach

## Slide 13: Winter Flight considerations
What are signs of Pitot Ice
  Airspeed indicator anomalies e.g. airspeed acts like an altimeter
What are signs if static air ice
  Static pressure port icing reduces reliability the airspeed indicator, rate-of-climb, and the altimeter.

## Slide 14: Winter Flight Freezing rain
Freezing rain occurs when snow travels through a large layer of warm air and melts into rain. It then hits a very thin layer of freezing cold air at the surface. Results in “Super Cooled Droplets” that freeze on impact. IMPACTS WINDSCREEN; TOTAL AIRFRAME; INCREASES STALL SPEED AND DRAG
What do we do?
Climb? Descend? Stay Level? Turn around?

## Slide 15: Winter Destination considerations
Notam’s for destination and alternate airports
  E.g. snow-covered taxiways and runways
  Runway slipperiness express for each third of the runway FICON REPORT, e.g. 5/5/5 is good, 1/1/1 is really bad
  Avoid use of brakes on a slippery runway and be cautious of runups while on ice
    The plane my slide during runup
Is preheat available at destination if staying for a while
Is jump starting available at the airport/aircraft maintenance

## Slide 16: Winter Flying Conclusions
It’s a beautiful time to fly
Requires a little extra planning
  For preparation
  Flight planning
  Destination considerations